## Slide 1
GO2cam V6.09 List of New Features
139 rue Vendôme, 69007 Lyon, France

## Slide 2
Licensing
Licences WAN
The type of licence is displayed in the Homepage
GO2cam V6.09 New Features
New typology of Licences
VAR
Production (end-users)
Educ
Dev and VAR: Modules and Options are automatically selected
Production and Educ need Bits
 Educ file cannot be read by a production licence
 Dev and VAR can read everything
Please read the dedicated document

## Slide 3
Installation
The update of software is not done anymore with patches.
New concept for the Update of software
Advantages:
The installation is fully automatic.
No more possible mistakes, due to manual modification of DAT files for example.
The update is done only with the command ‘Update Software’.
The user can choose whether he can update or not the version.
GO2cam V6.09 New Features
2 stages:
1. Do you want to update? Yes or No
2. If Yes, you can choose whether to exit the software now & run the update or to exit and update later manually.

## Slide 4
Launch
*.exe Launching
When launching GO2cam with the option -h, we display now a dialog box with all the available options.
GO2cam V6.09 New Features

## Slide 5
Homepage
Access for the 2 new modules of swiss machining
The type of licence is displayed in the banner.
GO2cam V6.09 New Features

## Slide 6
Files
Recent Files
While navigating in the recent files menu, we can now have a view of the workpiece in the*.PCE files
Save imported file
After importing a CAD file, some customers want to save the *.PCE file into the same directory. It can be done by checking the new option: ‘Save in the same directory as the imported file’.
6.08.210
14172 Abba
GO2cam V6.09 New Features

## Slide 7
CAD Import
Full associativity with Spaceclaim
& management of holes features
Spaceclaim file preview
GO2cam V6.09 New Features
Holes features recognition and update, Included in the dataGO option.

## Slide 8
New dialog box while using the ‘Part Update’ for FTE process.
- If you click in the box, you can see the corresponding holes in the screen,
- The dialog gives the following information:
  moved holes.
  modified holes (topology or size)
  the modified machining operations
- You can run the calculation of automatic holes.
FTE import
The name of the hole feature is now read and recovered while importing a file with FTE.
GO2cam V6.09 New Features
CAD Import

## Slide 9
New column ‘Color’ in the dialog box of multiple import, in order to identify easily the solids to be kept.
Multiple Import
GO2cam V6.09 New Features
CAD Import

## Slide 10
New dialog box to choose the version # while exporting in Parasolid (file and stock)
14164
The list of available export file is shorten.
Deletion of export in Catia V5, ACIS, VDA and DXF version 12.
CAD Export
Export X_T
GO2cam V6.09 New Features
CAD Export

## Slide 11
User Interface
RGB color becomes the standard in GO2cam.
You can still change the style in
Tools/Options/User Interface
 All the icons with systems of axis are also changed
Scale is now displayed in the screen
Interactive Axis System
GO2cam V6.09 New Features

## Slide 12
Deleted commands:
- Extremity Point
- Bounded  Unbounded
- Recovering the elements of a profile in geometry
New tooltips with HTML formatting ability
Menu Profiles
New Tooltips
V6.08
V6.09
The list of options for the measure on solid is now displayed in a combo box (in addition to the popup in background).
The options are also embellished with an explicit icon.
Control
GO2cam V6.09 New Features
User Interface

## Slide 13
New ability to draw geometry (wireframe and solid) by picking extremities of symbols.
You can also pick Z value directly on the symbol.
Picking symbol
Picking
New display for the picking of elements (wireframe-solid-symbols)
The extremity is highlighted by a small ball
The coordinates are displayed
An icon shows when the Z altitude is locked to a fixed value. There is no icon if the value is directly read on the geometry.
 It is also possible to define machining depths by clicking the symbol!
GO2cam V6.09 New Features
User Interface / Geometry

## Slide 14
V6.08
V6.09
Checkbox is replaced by the lock icon
Button to pick value is replaced by the pipette
New tooltip
Z Altitude Behaviour
GO2cam V6.09 New Features
User Interface / Geometry

## Slide 15
Dialog Area
Units are given in the field
The spinbox are added for all the fields
No more ENTER command to validate
GO2cam V6.09 New Features
User Interface / Wireframe
Display of icons in the combo box.

## Slide 16
Design
The command to retrieve erased elements is renewed and now offers a dialog box, where you can:
get the whole list of erased elements
filter the deleted elements by types
previsualize them on the screen.
Retrieve Erased Ref. Elements
GO2cam V6.09 New Features
Tick the checkbox to retrieve them and validate.

## Slide 17
Trim or Extend new function
10056 Jinfo
Chamfer / Fillet
Ability to choose a range of corners angles where to apply the element.
10972 GO2Fr
13693 GO2Gmbh
Bisector: option Z-level
13867 GO2Fr
GO2cam V6.09 New Features
Wireframe
Please read the dedicated document
Requests from VARs included in the Wireframe new module

## Slide 18
New dialog box for the Lofting command. It enables:
- The selection of profiles and guides
- Add / Delete / Invert / Modify order
- Button to previsualize the result
Holes Recognition
6.08.210
Lofting
We added a background color to the Technos tab to highlight the difference between tabs.
GO2cam V6.09 New Features
Solid Design
GO2 Gmbh

## Slide 19
Wire EDM Geometry
When a profile is deactivated in the tree, it is now also hidden in the screen.
Application of a color on faces that are still to be treated
The profile definition is accessible from the tree of profiles, in order to create a profile after having defined a Z section.
When a profile is created by a Z section, the profile definition enables to choose whether it is a die or a punch shape.
Recognition of Profiles
GO2cam V6.09 New Features

## Slide 20
Geometry Continuity is now automatically applied in the Solid Section
Solid Section
GO2cam V6.09 New Features
Wire EDM Geometry

## Slide 21
New command in the Edit menu which enables to change the workplane of wireframe or solid elements.
Change Plane
- By move:
the new plane is assigned to the elements, which are moved into the plane.
- By projection:
the new plane is assigned to the elements, and the elements stay as they are; their coordinates maybe 3D in that new plane.
2 modes are offered:
GO2cam V6.09 New Features
Workplanes

## Slide 22
11046 GO2Fr
The elements projected into a developed plane are not anymore transformed into polygons.
They are kept as arcs and segments, for a better machining result.
Dynamic Creation of Workplane
New icon to invert the direction of workplane.
Especially useful while creating a plane on a cylindric surface (cone, cylinder, hole,..)
14055 GO2Fr
Ability to give the X orientation by clicking 2 points
GO2cam V6.09 New Features
Workplanes
Developed Plane

## Slide 23
New commands that enable to save forming tools in XML format. Files are generated in file format *.OUF in XML.
Creation of Tools in XML
GO2cam V6.09 New Features
Module Forming Tool / Tools Libraries
Temporary Files
Milling and Turning holders by Revolution
This command is available for :
Form Tool,
Form Drill,
Form Insert,
Form Insert of Threading,
Form Insert of Whirling
The commands Save Temporary File and Recover Temporary File are added in this environment.

## Slide 24
GTC has been created because the ISO 13399 standard does not cover all the necessary information.
It provides an efficient exchange between the cutting tool vendor data and the applications.
Sandvik and Siemens are the initiators of the GTC.
- ISO 13399: Standard for the Cutting tool data representation and exchange
Standardization of Tools
- GTC format file (Generic Tool Catalog) is a complement to ISO 13399.
GO2cam tools are updated to be standardized according to:
GO2cam V6.09 New Features
Module Forming Tool / Tools Libraries

## Slide 25
New command to import tools from database in zip format (from GTC pack)
Ability to read the GTC files to import tools from many databases
Etc.
GO2cam V6.09 New Features
Module Forming Tool / Tools Libraries
Standardization of Tools

## Slide 26
Standardization / Homogenization of Tools
14324 GO2Fr
Clearance parameters are added
Drill
GO2cam V6.09 New Features

## Slide 27
Calculation of stages lengths homogenized with Level Drill
Better tracing of tool
Twin Edge Fine Boring Bar
GO2cam V6.09 New Features
Standardization / Homogenization of Tools

## Slide 28
Add of Mini Diameter (Dm) linked to the angle of insert (Kr)
Reference Kr of insert angle is added in the image and in the field
The display of insert is improved
13896 GO2Fr
11288 Saeilo
Face Mill Cutter
GO2cam V6.09 New Features
Standardization / Homogenization of Tools

## Slide 29
Clearance parameters are added
Side and Face Mill Cutter
Woodruff Cutter
- Parameter Tool Radius RE becomes RE1
- Parameter Top Radius (RE2) is added
- Parameter Tool Radius RE becomes RE1
- Parameter Top Radius (RE2) is added
14311 GO2Gmbh
14141 SysT
GO2cam V6.09 New Features
Standardization / Homogenization of Tools

## Slide 30
Chamfering Mill
Add of Cutting length (APMX) to define the shoulder on top of cone.
New image of tool
14403 GO2Fr
V6.08
V6.09
Double Chamfer Cutter
Add of Back Angle (BA)
GO2cam V6.09 New Features
Standardization / Homogenization of Tools

## Slide 31
Add of Shank Diameter (DCX)
¼ Circle Mill Cutter
Inverted Single-Angle
14311 GO2Gmbh
Add of Tool Radius (RE)
GO2cam V6.09 New Features
Standardization / Homogenization of Tools

## Slide 32
14486 Jinfo
Forming Tool / Forming Drill
Add of Overall length (LF)
New behaviour: there is now an automatic calculation of Overall length, Cutting length and Cut diameter according to the profile and dimension of the loaded file *.sym or *.ouf.
These values can be modified later on.
GO2cam V6.09 New Features
Standardization / Homogenization of Tools

## Slide 33
Tools Pages
The file chosen for the tool drawing is automatically copied into the directory ‘tool_picture’.
If the file already exists, you can rename it with a new dialog box (the addressing is not changed anymore!)
It is possible to open a DXF/DWG file as tool drawing.
The file is converted in JPG file formatet and displayed in the dialog.
The jpg file name will be DXF file + tool type extension
Example: drill.DXF -> drill_F20.JPG.
DXF/DWG as Tool drawing
GO2cam V6.09 New Features
Tool Drawing
Directory for Drawing selection

## Slide 34
We added a new option barcode that can be filled by the tools databases interfaces, according to standard EAN : European Article Numbering.
It is also available in the page of holders.
New user-field in the Options of tool. --> if a special code is defined in the tool, then it is written in the chosen technology. (number: in coolant nb / Chain in specific coolant)
6.08.210
GO2cam V6.09 New Features
Tools Pages
New field Barcode
New Coolant option in the Tool Page
GO2Gmbh

## Slide 35
Symbols
Download of libraries
14548 Saeilo
New possibility to import systems of axis from solid CAD files, by activating the option ‘Wireframe’.
GO2cam V6.09 New Features
Import of systems of axis
New ability to accede to the recent files selected in the libraries of:
Clamping elements (‘Vices and Clamps’)
Solid Holders (in the tools pages)
Very useful to create holders by importing STEP files from Sandvik, Iscar databases, etc. It enables to recover the systems of axis for the position of insert for example.

## Slide 36
Probing
3 new types of 2D corner probing:
It used to be done in 4 touches, 2 in X and 2 in Y.
Now we can probe a corner with:
2 touches in X and 1 touch in Y
1 touch in X and 2 touches in Y
1 touch in X and 1 touch in Y
2 new cycles:
Rectangular Block by 2 touches in the X axis
Rectangular Block by 2 touches in the Y axis
14121 Saeilo
14122 Saeilo
 It is now possible to click wireframe geometry
GO2cam V6.09 New Features
New Cycles for Origins on Stock

## Slide 37
New control report generated in XML format:
While using ‘Control of part’ probing cycles, all milling post-processors will be able to generate a control report in XML format file with the ISO name and the extension *.MEAS.
The file is automatically created in the same directory as NC files.
GO2cam V6.09 New Features
Probing
New Control Report

## Slide 38
- We can now probe the stock or the turning part in Turning environments.
- We can also select wireframe geometry to force special points to the probing. Then, the point is automatically projected on the solid according to the nearest normal direction.
- If we modify the coordinates of a point that has been probed (SHIFT+click), we automatically project these new coordinates on the solid.
GO2Fr
The interest to use Wireframe is the ability to use the silhouette positioned at Y=0.
GO2cam V6.09 New Features
Probing in Turning modules

## Slide 39
MTE
The main purpose of this function is to be able to manage tool gauges by external application. By this way the data can be managed by reading values from machine tool, from tool database, or from other sources.
In GO2cam V6.09, it is possible to update tool gauges by an external executable. To be able to do, the executable path has to be defined in the machine configuration.
If the “Controller communication utility” is defined, a button “Controller” will appear in the “Tools preparation” windows in Machine tooling menu.
GO2cam V6.09 New Features
MTE Tool offset Update

## Slide 40
When Clicking the button “Contrôleur” GO2cam will launch the executable file with two arguments.
First one is the path of xml file generated by GO2cam with information of mounted tools
Second one is the path of xml file waiting by GO2cam to update gauges
Sample : Gauge.exe “C:\GO2cam_Intl\GO2camV609\tmp\toolOut.xml” “C:\GO2cam_Intl\GO2camV609\tmp\toolIn.xml”
The toolIn.xml will have the same format than the toolOut.xml
To modify gauge value, the executable has to modify the concerned values (X,Y,Z) and set the State Attribute to “Modify”'
After treatment, the modified values will have a light green background
GO2cam V6.09 New Features
MTE
MTE Tool offset Update

## Slide 41
In the balanced operations, we added the new possibility to use 2 different tools !
GO2cam V6.09 New Features
MTE
Balanced operations: Opposite Tool
Behaviour:
Program the 4 axis balanced operation with one tool, as usually.
In the tree, in the tool popup, we added a new option ‘Different Opposite Tool’.
Here you can add the second tool or delete the one already chosen.
In MTE control, mount the 2 tools correctly. The list of tools inform about the 2 tools working in the same operation!

## Slide 42
GO2cam V6.09 New Features
MTE
Balanced operations: Opposite Tool
Notes:
The balloon tip in the tree gives the information of 2 tools
Standard simulation shows only the main tool! Only MTE simulation shows the 2 tools!

## Slide 43
Machining Generalities
Opelists Ref auto : modification of the Combo box Type of Line
Mute option is modified:
If a cycle of the opelist works with automatic references and that we cannot find the reference in the part, when a cycle is mute, it is automatically deleted and the opelist is calculated (formerly the opelist was set to warning)
GO2cam V6.09 New Features
Opelists
The number of flutes is now accessible to create and customize the list of operations.
14620 GO2cam Gmbh
Customize List of Operations

## Slide 44
Machining Generalities
We added the description of the materials ISO groups in the list; Cast Iron for K grade for example.
GO2cam V6.09 New Features
Material File
14367 Techsoft
Jump with TAB key is improved
Stock Dialog
Once launched, only the space bar and esc key had some effect: in V6.09, you can now use the buttons in the dialog to stop the simulation or change the speed for instance.
14263 GO2cam Gmbh
Toolpath Simulation

## Slide 45
Icon for the spindle rotation
While selecting machining operations, new ability to define ‘Bottom Z’ by clicking the symbol extremities.
It can be very useful to adjust the depth of machining according to the holding elements.
Altitudes and depths values are persistent !
GO2cam V6.09 New Features
Machining Generalities
Picking symbol
Technology Page

## Slide 46
GO2cam V6.09 New Features
Milling
Stock Calculation
New calculation:
Multi Threading is now used for the standard stock calculation. The more cores you have on the processor, the more rapid it is.
The algorithms are optimized.
 Calculation time is especially improved for 5 axis simultaneous toolpaths.
Part | V6.08 PC1 PC2 |  | V6.09 PC1 PC2 | V6.09
Finish facing ae1_standard.PCE | 4:49 | 7:18 | 1:27 | 1:31
Finish facing ae2_standard.PCE | 3:26 | 3:26 | 0:37 | 0:41
Finish Z level ap0.3_standard.PCE | 0:51 | 0:51 | 1:01 | 0:58
Rough facing ae3 ap3_standard.PCE | 0:08 | 0:10 | 0:03 | 0:04
 Faster Calculation + Better Calculation

## Slide 47
14236/14380 GO2Fr
When Gouge check is set to YES, we consider gouge check only for the 1st and last motions, and the intermediate motions defined in Movement page are now respected.
GO2cam V6.09 New Features
Milling
Pockets: Gouge Check and Movement Options

## Slide 48
Ability to define a negative radius value, in order to machine inverted fillet for a ‘slot’ with a Side and Face cutter.
GO2Fr
GO2cam V6.09 New Features
Milling
Contouring
Altitude on the bottom has a new name Input Altitude, because it now includes new options.
V6.08
V6.09
On bottom
Cavity
On tool top

## Slide 49
GO2Gmbh
GO2cam V6.09 New Features
Milling
Ability to use the ‘Inverted Single-Angle’ cutter with Pocket operation.
The purpose is to machine a bottom of pocket and tapered sides of pocket in one go.
This is why some parameters of pocket are automatically set and greyed out: Z step and steps ajustment, and Z allowance.
Pocket

## Slide 50
We can now pick an altitude by clicking directly a solid face.
If the face is not flat, we analyze the bounding box and we keep Zmax or Zmin according to the chosen icon.
Features
GO2cam V6.09 New Features
Milling
Face Mill cutter is added to the chamfering list of tools. Useful for Face mill with 45° inserts that can break angles
Chamfering
GO2cam France

## Slide 51
New option 3D correction
GO2cam calculates contact points and the vectors normal to the surface.
3D Correction for 5Xs isoparametric
7774 Jinfo
GO2cam V6.09 New Features
Milling
Toolpath
Contact
Post-processors do not manage this 3D correction right now.

## Slide 52
Management of 2 new tools:
Side end mill cutter
Woodruff cutter.
The Curve tolerance option is now used for the meshing of Parasolid surfaces.
In V6.08, this value ws fixed to 0.01 and not modifyable.
All the faces and surfaces are now updated during the toolpath calculation. If we move a solid or modify a face and that it is used for gouge checking, the toolpath will take it into account and be modified automatically.
Solution Korea
GO2cam V6.09 New Features
5 Axis Expert
New tools
Precision
Persistency of Solid Faces
Below, the bottom face is used for gouge checking: it is higher on the right side, where the toolpath is automatically modified.

## Slide 53
Wire EDM
14185 GO2Gmbh
The stop is now applied even if the stop length > last element length
Straight cut with Stop
GO2cam V6.09 New Features

## Slide 54
Turning Stock
14514 GO2Gmbh
When an axial milling cycle has consequences on the turning stock shape, it is now possible to take it into account for stock calculation of next turning operations.
For this, set on ‘Update of turning’ into the solid stock calculation option for each milling operation.
13979 Cam-Team
Turning stock manages axial milling cycles
This option is available only for milling cycles operating in the axial plane.
The red shape is machined by a pocket operation
Facing and Reaming take the stock after pocketting
GO2cam V6.09 New Features

## Slide 55
We can check the step and the direction of rotation of threads.
Turning Stock Rendering Texture
New rendering texture on the stock for the following machining operations:
Tapping
Die Threading,
Thread Whirling
Knurling
Standard Threading
Profile threading.
Rendering texture are also available in dynamic simulation for Tapping, Die Threading, Thread Whirling and Knurling.
GO2cam V6.09 New Features
Turning Stock

## Slide 56
Renew of P Point Calculation in all the turning cycles:
Toolpath calculation and simulation are not done anymore in Center Toolpath.
P Point Calculation
V6.08
V6.09
GO2cam V6.09 New Features
Turning

## Slide 57
List of resulting improvements:
Dynamic and Toolpath Simulations renew,
Coordinates given at P Point,
No more parasite motions.
V6.08
V6.09
GO2cam V6.09 New Features
Turning
Rapid Motions are correctly managed, with X and Z rectangular movements and not direct motions as formerly.
The Balanced Roughing and Balanced Finishing are also improved to manage correctly their moves in P Points Toolpath.
All the Approach/Return points are considered in P Points, if selected option. The coordinates of the given points are now generated in NC file.
Gouge check calculation is completely renew.
P Point Calculation

## Slide 58
14285 SysT
Bi-edges Tools
GO2cam V6.09 New Features
Turning
10699 Jinfo
In the Turn Face Cutter page, new parameter to calculate P Point position to standard or Bi-edges.

## Slide 59
We added 2 parameters to calculate the lateral passes:
in the tool page: Cutter width (CW)
in the strategy: Slot width
14224 Saeilo
Management of Grooves wider than Tool
The aim is to program several lateral passes in Y, if the groove if wider than the tool
GO2cam V6.09 New Features
Broaching

## Slide 60
New option Cone Angle to enable a sloped return motion. Especially useful when the slot is blind.
Improvement of rapid toolpath while indexing with a new motion of positioning to enable to turn round as on the machine
14224 Saeilo
GO2cam V6.09 New Features
Broaching
Improvements

## Slide 61
New Management of Chip Breaking
14192 GO2Gmbh
turnyuGO
Add of the dwell for chip breaking in the motions of Profile Retraction type:
- we delete the retracts on the profile following
- we activate the dwell on the profile retraction if the retract is set to 0
- We activate the dwell if we do not machine pockets.
13911 GO2Fr
GO2cam V6.09 New Features
Turning
We use a retract to 45° to manage chip breaking. As for roughing, we use the length of cut to run the retract and a retract value. Leadin can be done either linear or circular.
Roughing

## Slide 62
13639 GO2Gmbh
New method ‘in flat bottom’ to calculate the overlap, in order to minimize the toolpath.
Groove Finishing
GO2cam V6.09 New Features
Turning
Endless Screw
Finishing of a Screw: we added the finish parameter such as in the grooving operations

## Slide 63
Strategy dialogs are renewed
New parameter Dwell
Management of live tools rotation coupled with the spindle rotation. Used to respect the cutting conditions for small tools by adding tool rotation and spindle rotation.
Centering / Tapping
Tapping
Centering / Drilling
Management of the 4th point of a level drill has been added.
Drilling
GO2cam V6.09 New Features
Turning

## Slide 64
New parameter, dedicated to swiss machining: Deburring length is useful to cut the chip on the bar to avoid injuring the guide bush.
14098
Roughing
GO2cam V6.09 New Features
Turning / Swiss Machining
Synchro
New Techno cycle to define synchro between 2 cycles. More flexible and easy to use than the Synchro diagram.

## Slide 65
  Form Finishing
  Knurling
Finishing operation done forming tools, especially for Back turning tools.
*.sym and *.ouf tools can be used.
*.ouf is a new format file to draw forming tools and save them into xml format.
Libraries of ISCAR and KYOCERA tools are available.
Knurling is a machining operation that consists in creating combination of horizontal, vertical or crossing lines on the surface of material.
13924 Saeilo
4 new cycles
GO2cam V6.09 New Features
Turning / Swiss Machining

## Slide 66
  Die Threading
  Thread Whirling
Operation similar to a tapping operation but for a shaft.
Thread whirling is similar the a thread milling process, except that inserts are mounted on the inside of a cutting ring.
The ring turns around the part to machine the thread in one pass
Thread whirling is a productive method and often used for special thread forms that need to be produced quickly and at high tolerances. Typical components are medical bone screws, implants, feed screws, worm gears, and other micro components.
Use of a threading die tool.
4 new cycles
GO2cam V6.09 New Features
Turning / Swiss Machining

## Slide 67
- 2 new modules
- Process with a Wizard (such as MPM) that will enable the choice of machine.
- Machine File
New Machine File Format: *.MCS
New Standard PPs: *.SPS
Swiss Machining Classic: turning + milling + 4 axis with C and Y
Swiss Machining Expert: Classic + B axis + 3D milling
Dedicated to sliding headstock
GO2cam V6.09 New Features
Swiss Machining Modules

## Slide 68
NC File
Former standard PPS (<V6) are now archived in ppstd\lib.
The list of available PPs is reduced at first sight.
GO2cam V6.09 New Features

## Slide 69
Workshop documents
Workshop Doc and PDF workshop doc are not anymore external application, there are fully included in the software.
Consequently, running those commands is much more faster and reliable than used to be.
Also, it deals with the part on the current session!
In the page Customized Documents, the checkbox are greyed out if the corresponding XML (A3H.xml , ...) are not in the directory Model.
GO2cam V6.09 New Features
Customized Documents
The bitmap is also now displayed in the list of available pages

## Slide 70
A new option enables to choose whether you want 3D model or just an image.
Display of tools is improved.
GO2cam V6.09 New Features
Workshop documents
Tools Pages

## Slide 71
Homogenizing of User Workshop Docuemnt compared to standard command regarding the display of part in 3D
- UWD has now the toolbar to hide/display the different types of solid
- The screenshot in background is shown while deactivating the 3D mode
- The default view is ZX for turning part
GO2cam V6.09 New Features
3D Display
User Workshop documents

## Slide 72
The answers to the user questions are now saved in tmp/documentationAnswer.ini for each model, to be suggested the next time by default
Pages to be filled
User questions and Title block now appear in a combo box.
We do not create severak pages anymore if the number of questions was exceeding 12.
GO2cam V6.09 New Features
User Workshop documents

## Slide 73
GO2Fr 13911
We can now change the order of pages by the popup menu. The list must be ordered by first column if you want those items to appear.
GO2cam V6.09 New Features
Workshop documents / UWD
Pages Manager

## Slide 74
GO2cam for SW
- Save Button is added on top bar
- Ability to keep the CAD tree into the CAM menu
- Request to have the ability to copy some / or all cycles from one GO2cam instance into another. Copy opelist directly from file does not work with SLDPRT files.
For this, you need to open the file called ini\PlugIns.ini in the directory where is installed the plugin (for instance C:\GO2cam_Intl\GO2camV608\System\GO2SW).
Check the option FeatureManagerOpen=0. Set it to 1 to keep the tree and launch the software again.
GO2cam V6.09 New Features