## Slide 1: GO2cam V6.09
5 Axis Expert
The General Mode

## Slide 2
5 Axis Expert: The General Mode
Implementation: Selection and Process
1.Surface Paths
2. Tool axis control
3. Gouge check
4. Link
5. Roughing
6. Utility

## Slide 3
5 Axis Expert: The General Mode
Implementation
Always program the toolpath in the REFERENCE plane: the orientation of tool is given in the 5 axis strategy dialogs
Important Rule

## Slide 4
5 Axis Expert: The General Mode
Implementation / Selection
Selection: same as standard cycles with the 3 steps, but some specific rules:
Selection of the faces to machine.
Warning: the selection is not ended at this point: most of the toolpath patterns need pilot curves or surfaces, they have to be selected inside the tab ‘Surface Paths’.
The choice of tool (or tool familly) must be done before the selection of machining.
Choice of the machining operation

## Slide 5
5 Axis Expert: The General Mode
Selection: process to select faces
During the selection, the modes can be combined for a better efficiency.
Selection by click
Selection by window
Click an edge
Define an edges path
Validate the choice of faces or choose opposite faces
Selection by edges path
Implementation / Selection

## Slide 6
5 Axis Expert: The General Mode
Implementation / Selection
Selection by Brush: select the faces by ‘flying’ over them with the mouse.
Use Ctrl key to add faces,
Use Shift key to delete faces.
Selection: process to select faces

## Slide 7
5 Axis Expert: The General Mode
Implementation / Process
Process: tabs from left to right  Calculate each step then adjust calculation  go next step
1
2
3
1. Select the faces and create a toolpath without thinking about the tool!
2. Once the toolpath looks good, work on the tool direction!
3. Once the toolpath and tool settings are ok, choose a gouge control strategy and recalculate toolpaths.

## Slide 8
5 Axis Expert: The General Mode
Implementation / Process
1
2
3
1. create a toolpath
2. work on the tool direction!
3. choose a gouge control strategy.
01 - 5X Sample.PCE

## Slide 9
5 Axis Expert: The General Mode
1. Surface Paths - Patterns
The pattern enables the choice of Types of Cuts (not the concept of machining cycle)
Solid faces alone
Solid faces + guide
Guide= surface or curve
Drive Surfaces for next examples
Note: ‘curves’ can be open or closed, 2D geometry or curve

## Slide 10
5 Axis Expert: The General Mode
1. Surface Paths - Patterns
Parallel Cuts: slices are parallel to each other.
Use:
Facing
Helix toolpath
Contouring
02 - Parallel cuts.PCE

## Slide 11
5 Axis Expert: The General Mode
1. Surface Paths - Patterns
Cuts along curve: tool path is orthogonal to a drive curve.
Use: Follow a special shape
Design of the curve in GO2cam

## Slide 12
5 Axis Expert: The General Mode
1. Surface Paths - Patterns
Morph between 2 curves: toolpath is a morphing done between 2 curves.
Use:
Any surface correctly bounded by curves.
Finishing of fillets, slots, etc.
The 2 curves are not used as a limitation area!
03 - 5X Trimming between 2 curves.PCE

## Slide 13
5 Axis Expert: The General Mode
1. Surface Paths - Patterns
Parallel to multiple curve: toolpath stays parallel to one or several drive curve(s).
Use:
All cuts stay parallel to the curve.
In case of one curve, the toolpaths always starts at the opposite side.
It is not a copy, each offset is done according to the previous path!
04 - 5Xs parallel to curve.PCE

## Slide 14
5 Axis Expert: The General Mode
1. Surface Paths - Patterns
Project curve: the curve chosen is projected on the surface shown.
Use:
Engraving, marking…

## Slide 15
5 Axis Expert: The General Mode
1. Surface Paths - Patterns
Morph between 2 surfaces: toolpath is a morphing done between 2 surfaces.
Use:
Any surface correctly bounded by other faces
Slot with taper flanks
Fillets, etc.
Impeller bottom

## Slide 16
5 Axis Expert: The General Mode
1. Surface Paths - Patterns
Parallel to surface: the toolpath is done parallel to another chosen surface (pointed out with the arrow)
The leadin surface gives the shape of the toolpath
Leadin Surface

## Slide 17
5 Axis Expert: The General Mode
1. Surface Paths - Patterns
How to choose?
1. Morphing toolpaths are always good and smooth toolpaths for any shape.
2. Parallel toolpaths require more regular or symmetrical surfaces and guides.
3. Parallel cuts pattern is chosen for facing or contouring.
4. Project curve and Cut along curve are very specific toolpaths.

## Slide 18
5 Axis Expert: The General Mode
1. Surface Paths - Patterns
Choosing a pattern with curves is always longer and more difficult process:
creation of edges then Geometry continuity or Curves to arc function must be done.
Be very careful to the creation of ‘curve’
 Here, choose ‘Face’ option instead of ‘Edge’

## Slide 19
5 Axis Expert: The General Mode
1. Surface Paths - Dialog
1. Pattern of toolpaths, selection of edges and surfaces.
2. Machining Area
(limitation area, angles range, etc.)
3. Toolpath Adjustment
(1 way or zigzag, start point, etc.)
4. Surface quality: 0.1 is enough for roughing.
1
2
3
4
5
5. Stepover and relative crest value.

## Slide 20
5 Axis Expert: The General Mode
1. Surface Paths - Tips
Use the Start and end margins to fix possible problems of tolerances.
Margins
Margin = 0.1
05 – Compressor1.PCE

## Slide 21
5 Axis Expert: The General Mode
1. Surface Paths - Tips
Internal tool radius
The toolpath is modified and shifted from the radius value, so that it is in tangency with side surface.
06 - Internal tool radius.PCE

## Slide 22
5 Axis Expert: The General Mode
1. Surface Paths - Tips
It can be useful to fix problems of accuracy of edges by merging surfaces.
You can choose a fixed value or a percent of tool diameter.
 Also useful to go through pockets or holes!

## Slide 23
5 Axis Expert: The General Mode
2. Tool Axis Control
Contrary to the standard machining selection in GO2cam, the tool orientation is not linked to the machining plane: it can be, but it can also be relative to the surface to machine or to any geometric element (curve, point).
Maximum angle step
Number of axis
- Maximum allowed angle change
- Definition of the resolution of the map for collision checking.

## Slide 24
5 Axis Expert: The General Mode
2. Tool Axis Control
Tilting Strategies
Parameters changing according to the chosen Tilting Strategy

## Slide 25
5 Axis Expert: The General Mode
2. Tool Axis Control
Tilt angle at side of cutting direction
When Tilt angle=90°
 Maxi Stepover= Z step
07 – Tool Control.PCE

## Slide 26
5 Axis Expert: The General Mode
2. Tool Axis Control
Pilot Tool

## Slide 27
5 Axis Expert: The General Mode
2. Tool Axis Control
When the tool turns around itself, it is because it is ‘lost’ regarding the UV curves of the surface.
Advanced / Ruled Surface Radius Limit:
enter 0 or 99999 to force the choice of one direction.
Machining Vector:
You can set the length in Tools/Options/Graphic window
You can also hide the vector in the Machining tree with a right-click on the toolpath.
08 – Compressor2.PCE

## Slide 28
5 Axis Expert: The General Mode
3. Gouge check (Collision Avoidance Strategies)
In addition, up to four separate check surface groups can be selected and individual gouge avoidance strategies can be applied to each successive group.
The user can specify not one, but four different tool gouge strategies to a single operation.
Retraction Strategies
Surface groups
Tool Elements gouge checking

## Slide 29
5 Axis Expert: The General Mode
4. Link
Definition of strategies
Values used in the strategies
Definition of Leadin and Leadout strategies, links between passes in XY and Z, clearances values, feed and rapid distances, etc.

## Slide 30
5 Axis Expert: The General Mode
4. Link - Strategies
Leadin & Leadout
Gaps along cut
Small and large gaps strategies.

## Slide 31
5 Axis Expert: The General Mode
4. Link - Strategies
Links between slices
‘Slices’ are passes in XY: many different strategies for small and large moves.
Links between passes
Passes are done in Z: many different strategies for small and large moves.
Appears if Depth cuts
is checked ON (page Roughing)

## Slide 32
5 Axis Expert: The General Mode
4. Link – Values in Strategies
For screw and any cylindrical shape, choose Cylinder Type to define the approaches and retracts.

## Slide 33
5 Axis Expert: The General Mode
4. Link – Values in Strategies

## Slide 34
5 Axis Expert: The General Mode
5. Roughing
Definition of stock
Use of GO2cam stock:
Original stock or
Last calculated stock (in case of roughing and if stock calculation is ON)
STL file: you can import the file in STL saved after calculation of roughing operation (STL can be saved in the simulation dialog)
09 - Stock testing.PCE

## Slide 35
5 Axis Expert: The General Mode
5. Roughing
Multi passes are passes done on the side of Drive Surface
Management of cuts

## Slide 36
5 Axis Expert: The General Mode
5. Roughing
Management of cuts
Depth cuts are the defined in the direction of tool axis.

## Slide 37
5 Axis Expert: The General Mode
6. Utility
Extra functions
Feed rate control: tool axis.
Axial shift: shift of the toolpath in the tool axis direction.
Toolpath
Shift

## Slide 38
5 Axis Expert: The General Mode
6. Utility
5X Trimming
Swarf? NO: impossible to get the right orientation…
Process:
1. Creation of curves
2. Morph between curves / Tilt 0°
3. Morph between curves / Tilt 90°
4. Utility / Axial shift -3 mm
03 - 5X Trimming between 2 curves.PCE