## Slide 1: MTE pattern for swiss machining

## Slide 2: Summary
1. Introduction
2. Machine sample
3. Part programming
4. Demonstration
5. Conclusion
6. Q&A

## Slide 3: Summary
1. Introduction
2. Machine sample
3. Part programming
4. Demonstration
5. Conclusion
6. Q&A

## Slide 4: 1. Introduction
What is pattern in Swiss Machining ?
  Manage machine with more than 2 channels
  It describes to the CN which axes will be driven by channels

## Slide 5: 1. Introduction
The pattern codes
  synchronize channels
  can be M or G code depending of machine builders

## Slide 6: Summary
1. Introduction
2. Machine sample
3. Part programming
4. Demonstration
5. Conclusion
6. Q&A

## Slide 7: 2. Machine sample
Swiss machine :
  2 spindles
  3 racks
  3 channels

## Slide 8: 2. Machine sample
Rack 1 works on main spindle
  Z1 and X1 are driven

## Slide 9: 2. Machine sample
Rack 2 works on sub spindle
  Z2 and X2 are driven

## Slide 10: 2. Machine sample
Rack 3 can work on main spindle
Z3 locked
X3 and Z1 are driven
Z1 locked
X3 and Z3 are driven

## Slide 11: 2. Machine sample
Rack 3 can work on sub spindle:
Z3 locked
X3 and Z2 are driven
Z2 locked
X3 and Z3 are driven

## Slide 12: 2. Machine sample
Pattern Table : Defined in the MCG file of swiss machine
Pattern | Channel 1 | Channel 2 | Channel 3
G610 | X1, Z1 | X3, Z3 | X2, Z2
G620 | X3, Z1 |  | X2, Z2
G630 | X1, Z1 |  | X3, Z2

## Slide 13: Summary
1. Introduction
2. Machine sample
3. Part programming
4. Demonstration
5. Conclusion
6. Q&A

## Slide 14: 3. Part programming

## Slide 15: 3. Part programming
MS - Facing
MS – Pre Drill
MS - Drill
MS – External Finish 1
MS – Finish Groove
MS – External Finish 2
Parting
Part Rework
SS - Facing
SS – External Finish
SS – O Ring Type
SS - Drilling
Channel 1 | Channel 2 | Channel 3

## Slide 16: 3. Part Programming
MS – Facing
MS - Facing
Pattern | Channel 1 | Channel 2 | Channel 3
G610 | X1, Z1 | X3, Z3 | X2, Z2
G620 | X3, Z1 |  | X2, Z2
G630 | X1, Z1 |  | X3, Z2
MS – Facing
X1, Z1
Tool mounted on rack 1

## Slide 17: 3. Part programming
Channel 1 | Channel 2 | Channel 3
MS - Facing
MS – Pre Drill
MS - Drill
MS – External Finish 1
MS – Finish Groove
MS – External Finish 2
Parting
Part Rework
SS - Facing
SS – External Finish
SS – O Ring Type
SS - Drilling

## Slide 18: 3. Part Programming
MS – Pre Drill : solution 1
MS – Pre Drill
Pattern | Channel 1 | Channel 2 | Channel 3
G610 | X1, Z1 | X3, Z3 | X2, Z2
G620 | X3, Z1 |  | X2, Z2
G630 | X1, Z1 |  | X3, Z2
MS – Pre Drill
X3, Z3
Lock Z1
Tool mounted on rack 3

## Slide 19: 3. Part programming
Channel 1 | Channel 2 | Channel 3
MS - Facing
MS – Pre Drill
MS - Drill
MS – External Finish 1
MS – Finish Groove
MS – External Finish 2
Parting
Part Rework
SS - Facing
SS – External Finish
SS – O Ring Type
SS - Drilling

## Slide 20: 3. Part Programming
MS – Pre Drill : solution 2
MS – Pre Drill
Pattern | Channel 1 | Channel 2 | Channel 3
G610 | X1, Z1 | X3, Z3 | X2, Z2
G620 | X3, Z1 |  | X2, Z2
G630 | X1, Z1 |  | X3, Z2
MS – Pre Drill
X3, Z1
Lock Z3
Tool mounted on rack 3

## Slide 21: 3. Part programming
Channel 1 | Channel 2 | Channel 3
MS - Facing
MS – Pre Drill
MS - Drill
MS – External Finish 1
MS – Finish Groove
MS – External Finish 2
Parting
Part Rework
SS - Facing
SS – External Finish
SS – O Ring Type
SS - Drilling

## Slide 22: 3. Part Programming
Sub Spindle
SS – Facing
Pattern | Channel 1 | Channel 2 | Channel 3
G610 | X1, Z1 | X3, Z3 | X2, Z2
G620 | X3, Z1 |  | X2, Z2
G630 | X1, Z1 |  | X3, Z2
SS – Facing
X2, Z2
Tool mounted on rack 2

## Slide 23: 3. Part programming
Channel 1 | Channel 2 | Channel 3
MS - Facing
MS – Pre Drill
MS - Drill
MS – External Finish 1
MS – Finish Groove
MS – External Finish 2
Parting
Part Rework
SS - Facing
SS – External Finish
SS – O Ring Type
SS - Drilling

## Slide 24: 3. Part Programming
SS – Drilling : Solution 1
SS - Drilling
Pattern | Channel 1 | Channel 2 | Channel 3
G610 | X1, Z1 | X3, Z3 | X2, Z2
G620 | X3, Z1 |  | X2, Z2
G630 | X1, Z1 |  | X3, Z2
SS - Drilling
X3, Z2
Lock Z3
Tool mounted on rack 3

## Slide 25: 3. Part programming
Channel 1 | Channel 2 | Channel 3
MS - Facing
MS – Pre Drill
MS - Drill
MS – External Finish 1
MS – Finish Groove
MS – External Finish 2
Parting
Part Rework
SS - Facing
SS – External Finish
SS – O Ring Type
SS - Drilling

## Slide 26: 3. Part Programming
SS – Drilling : Solution 2
SS - Drilling
Pattern | Channel 1 | Channel 2 | Channel 3
G610 | X1, Z1 | X3, Z3 | X2, Z2
G620 | X3, Z1 |  | X2, Z2
G630 | X1, Z1 |  | X3, Z2
SS - Drilling
X3, Z3
Lock Z2
Tool mounted on rack 3

## Slide 27: 3. Part programming
Channel 1 | Channel 2 | Channel 3
MS - Facing
MS – Pre Drill
MS - Drill
MS – External Finish 1
MS – Finish Groove
MS – External Finish 2
Parting
Part Rework
SS - Facing
SS – External Finish
SS – O Ring Type
SS - Drilling
Parting
Parting
Part Rework
Part Rework

## Slide 28: 3. Part programming
Channel 1 | Channel 2 | Channel 3
MS – Facing : X1, Z1
MS – Pre Drill : X3, Z1
MS – Drill : X3, Z1
MS – External Finish 1 : X1, Z1
MS – Finish Groove : X1, Z1
MS – External Finish 2 : X1, Z1
Parting
Part Rework
SS – Facing : X2, Z2
SS – External Finish : X2, Z2
SS – O Ring Type : X2, Z2
SS – Drilling : X3, Z3
Parting
Parting
Part Rework
Part Rework

## Slide 29: 3. Part programming
Channel 1 | Channel 2 | Channel 3
MS – Facing : X1, Z1
MS – Pre Drill : X3, Z1
MS – Drill : X3, Z1
MS – External Finish 1 : X1, Z1
MS – Finish Groove : X1, Z1
MS – External Finish 2 : X1, Z1
Parting
Part Rework
SS – Facing : X2, Z2
SS – External Finish : X2, Z2
SS – O Ring Type : X2, Z2
SS – Drilling : X3, Z3
Parting
Parting
Part Rework
Part Rework
Initialization
Change
Change

## Slide 30: 3. Part programming
Channel 1 | Channel 2 | Channel 3
MS – Facing : X1, Z1
MS – Pre Drill : X3, Z1
MS – Drill : X3, Z1
MS – External Finish 1 : X1, Z1
MS – Finish Groove : X1, Z1
MS – External Finish 2 : X1, Z1
Parting
Part Rework
SS – Facing : X2, Z2
SS – External Finish : X2, Z2
SS – O Ring Type : X2, Z2
SS – Drilling : X3, Z3
Parting
Parting
Part Rework
Part Rework
Initialization
Change
Change
G610
G620
G610

## Slide 31: Summary
1. Introduction
2. Machine sample
3. Part programming
4. Demonstration
5. Conclusion
6. Q&A

## Slide 32: 4. Demonstration
For each operation with tool mounted on rack 3
  Choose which axis will be locked

## Slide 33: 4. Demonstration
Synchronization definition

## Slide 34: 4. Demonstration
Pattern set
  List of compatible patterns displayed
  Autocreation of synchronizations in channel if necessary

## Slide 35: 4. Demonstration
Pattern set
  Detection of pattern incompatibility

## Slide 36: 4. Demonstration
NC output with synchronization

## Slide 37: Summary
1. Introduction
2. Machine sample
3. Part programming
4. Demonstration
5. Conclusion
6. Q&A

## Slide 38: 5. Conclusion
Workflow to output NC program with Pattern
1 : Pattern of machine set in MCG
2 : Program the part as usually in GO2cam

## Slide 39: 5. Conclusion
3 : Mount the tools on the racks
4 : Locking of axes

## Slide 40: 5. Conclusion
5 : Synchronize
6 : Define patterns

## Slide 41: 5. Conclusion
7 : Output NC

## Slide 42: Summary
1. Introduction
2. Machine sample
3. Part programming
4. Demonstration
5. Conclusion
6. Q&A

## Slide 43: 6. Q&A
Thank you for your attention

## Slide 44: THANK YOU
139 rue Vendôme – 69006 – Lyon, France